## Slide 1: JUST-IN-TIME COMPILATION
Lessons Learned From Transmeta
Thomas Kistler
thomas.kistler@smachines.com

## Slide 2: Industry Observation
Shift away from proprietary closed platforms to open architecture-independent platforms
Shift away from native code to portable code
All these platforms make heavy use of just-in-time compilation

## Slide 3: Industry Observation
Examples
  Android & Dalvik VM
  Chromium OS & PNaCl
  Java ME/SE/EE & Java VM
  HTML5 & JavaScript
  Microsoft .NET & CLR
  VMWare

## Slide 4
Part I
The Transmeta Architecture

## Slide 5: Transmeta’s Premise
Superscalar out-of-order processors are complicated
Lots of transistors
Increased power consumption
Increased die area
Increased cost
Do not scale well

## Slide 6: Transmeta’s Idea
Build simple in-order VLIW processor with Code Morphing Software
More efficient in area, cost and power
Performance of out-of-order architecture through software optimization

## Slide 7: VLIW Architecture
In superscalar architectures, the execution units are invisible to the instruction set. The instruction set is independent of the micro-architecture.
In VLIW architectures, the execution units are visible to the instruction set. A VLIW instruction encodes multiple operations; specifically, one operation for each execution unit. The instruction set is closely tied to the micro-architecture.
No or limited hardware interlocks. The compiler is responsible for correct scheduling.
No forward and backward compatibility.

## Slide 8: Software Architecture
x86 Code
Interpreter

## Slide 9: Software Architecture
Code Cache
x86 Code
Translated?
Interpreter
Hot?
Just-in-Time Compiler
VLIW Code
VLIW Code
VLIW Code
Yes
No
No
Yes

## Slide 10: Software Architecture
Code Cache
Yes
x86 Code
Translated?
Interpreter
Hot?
Just-in-Time Compiler
VLIW Code
VLIW Code
VLIW Code
No
No
Yes

## Slide 11: Translation Example
ld %r30,[%esp] add.c %eax,%eax,%r30 ld %r31,[%esp] add.c %ebx,%ebx,%r31 ld %esi,[%ebp] sub.c %ecx,%ecx,5
ld %r30,[%esp] add %eax,%eax,%r30 add %ebx,%ebx,%r30 ld %esi,[%ebp] sub.c %ecx,%ecx,5
{ ld %r30,[%esp];
sub.c %ecx,%ecx,5 }
{ ld %esi,[%ebp];
add %eax,%eax,%r30;
add %ebx,%ebx,%r30 }
addl %eax,(%esp) addl %ebx,(%esp) movl %esi,(%ebp) subl %ecx,5
Original Code
Translated Code
Optimized Code
VLIW Code

## Slide 12: Software Advantages
Moves complexity from hardware to software.
Can optimize a large group of instructions.
Optimization cost is amortized. Out-of-order hardware pays the cost every single time.
Avoids legacy code problem.
More speculation is possible with proper hardware support.

## Slide 13: Speculation
{ ld %r30,[%esp];
sub.c %ecx,%ecx,5 }
{ ld %esi,[%ebp];
add %eax,%eax,%r30;
add %ebx,%ebx,%r30 }
addl %eax,(%esp) addl %ebx,(%esp) movl %esi,(%ebp) subl %ecx,5
Original Code
VLIW Code
Problem
Exceptions are precise. What if ld faults? The sub executes out-of-order.

## Slide 14: Speculation
Solution
Commit
  All registers are shadowed (working and shadow copy). Normal instructions only update working copy. When translation is done, a commit instruction is issued and all working registers are copied to their shadows
Rollback
  If an exception happens, a rollback instruction is issued. All shadow registers are copied to the working set and software re-executes the x86 code conservatively

## Slide 15: Speculation
{ ld %r30,[%esp] }
{ st %eax,[%esi] }
{ ld %r31,[%esp] }
{ st %eax, [%esp] } { ld %esi, [%ebp] } { sub.c %esi,%esi,5 }
Load Speculation
Load/Store Elimination
Moving loads above stores can be a big scheduling benefit.
Eliminate redundant loads.
Problem
It is hard to prove that load and store addresses do not conflict.

## Slide 16: Speculation
Solution
Load And Protect
  Loads are converted to load-and-protect. They record the address and data size of the load and create a protected region.
Store Under Alias Mask
  Stores are converted to store-under-alias-mask. They check for protected regions and raise an exception if there is an address match.

## Slide 17: Speculation
{ ld %r30,[%esp] }
{ st %eax,[%esi] }
{ ld %r31,[%esp] }
{ st %eax, [%esp] } { ld %esi, [%ebp] } { sub.c %esi,%esi,5 }
Load Speculation
Load/Store Elimination
{ ldp %r30,[%esp] }
{ stam %eax,[%esi] }
{ copy %r31,%r30 }
{ ldp %esi, [%ebp] } { stam %eax, [%esp] } { sub.c %esi,%esi,5 }

## Slide 18: Self-Modifying Code
Problem
What if x86 code changes dynamically? Existing translations are probably wrong!

## Slide 19: Self-Modifying Code
Solution
T-Bit Protection
  Software write-protects the pages of x86 memory containing translations with a special T-bit. Hardware faults for writes to T-bit protected pages. Software then invalidates all translations on that page.

## Slide 20: Self-Modifying Code
Different types of self-modifying code
  Windows BitBlt
  Shared code and data pages
  Code that patches offsets and constants
  Just-in-time compilers. Generating code in code cache, garbage collecting code, patching code, etc.

## Slide 21
Part II
Lessons Learned

## Slide 22: Software Out-of-Order
Questions
  Can software speculation using commit/rollback and load-and-protect/store-under-mask significantly improve performance over traditional in-order architectures?
  Can software speculation eliminate memory stalls (memory stalls are very expensive in modern CPU architectures) to compete with out-of-order architectures?

## Slide 23: Lesson 1
Software speculation cannot compete with true out-of-order performance in terms of raw performance.

## Slide 24: Snappiness
Questions
  What is the relationship between translation overhead and performance?
  What is the relationship between snappiness and steady-state performance?

## Slide 25: Gears Overview
1st Gear (Interpreter)
  Executes one instruction at a time. Gathers branch frequencies and direction. No startup cost, lowest speed.
2nd Gear
  Initial translation. Light optimization, simple scheduling. Low translation overhead, fast execution.
3rd Gear
  Better translations. Advanced optimizations. High translation overhead, fastest execution.

## Slide 26: Gears Costs
 | Startup Cost (Cycles/Instruction) | Performance (Cycles/Instruction) | Trigger Point (# Executions)
Gear 1 | 0 | 100.0 | -
Gear 2 | 8,000 | 1.5 | 50
Gear 3 | 16,000 | 1.2 | 10000

## Slide 27: Gears CPI (Clocks per Instruction)

## Slide 28: Application Behavior Static Analysis

## Slide 29: Application Behavior Dynamic Analysis

## Slide 30: Application Behavior Dynamic Analysis – Cumulative

## Slide 31: Application Behavior Cycle Analysis

## Slide 32: Application Behavior Cycle Analysis

## Slide 33: Application Behavior Cycle Analysis – Alternative I

## Slide 34: Application Behavior Cycle Analysis – Alternative II

## Slide 35: Lesson 2
The first-level gear is incredibly important for perceived performance and snappiness. The interpreter is not good enough.
Higher-level gears are incredibly important for steady-state performance.

## Slide 36: Interrupt Latency
Questions
  When do we generate the translated code and how do we interrupt the “main x86 thread”?
  How does the design of the translator affect real-time response times or interrupt latencies?
  How does the design of the translator affect soft real time applications?

## Slide 37: Interrupt Latency
Transmeta’s Answer
  The main “x86 thread” is interrupted and the translation is generated in-place. The main “x86 thread” then resumes.
  Problem
  Generating a highly optimized translation can consume millions of cycles, during which the system appears unresponsive.

## Slide 38: Lesson 3
The design of a just-in-time compiler must be multi-threaded. The system must guarantee a certain amount of main “x86 thread” forward progress. The optimization thread(s) must run in the background (or on a different core) and must be preemptable.

## Slide 39
Part III
Questions?

## Slide 41: SMWare
We are Always Looking for Talent!
Thomas Kistler
thomas.kistler@smachines.com